## Slide 1: The impact of pedestrians on roundabout‘s entry
A simulation in the context of the lecture, Modelling and Simulating Social Systems with MATLAB

## Slide 2: Introduction
Research Question:
Is a reasonably small increase of the storage space between the yield line and the crosswalk “n_a “ has a significant positive impact on the entry capacity “Cs” ?
n_a

## Slide 3: Gap acceptance theory
Entry-capacity Cs: How many vehicles can enter one accepted gap and how accepted gaps are provided
Minorflow: Vehicles intending to merge into the roundabout
Majorflows: Pedestrians crossing and circulating vehicles
Roundabout  two unsignalized intersections to cross and merge into.
Fig. 1

## Slide 4: The model
Circulation flow divided in flowing traffic (Ca) queuing traffic ( Pq)
Ca(n_a) is adjusted with f and g
f = maximum entry flow without considering pedestrians ( simple case )
g = maximum entry flow considering pedestrians but without storage space ( calculated using Queue theory )
Pq is estimated using queuing theory
Fig. 2

## Slide 5: The implementation
Two different Implementation
First shows the impact of a growing n_a
Second shows the difference between n_a =1 and n_a =2 over a day.

## Slide 6: Results and Discussion
Fitting parameters because of the simplified model
Values in the same range as in the model from Dr. Eng. Nan Kang and Dr. Eng. Hideki Nakamura
A big change of cs from n_a = 1 n_a= 2

## Slide 7: Results and Discussion
Impact of n_a remains for changing q_c
n_a = 2 is the most promising value

## Slide 8: Results and Discussion
First implementation was not very accurate
q_c, q_cprime, q_p and q_pprime variate over 24 hours
Only an improvement of 11 percent over a day
Big improvement between 10am and 5pm

## Slide 9: Results and Discussion
Behaves as expected and correlates
Model is highly symplified but still gives consistent results
n_a might have a big influence
Next step real Data

## Slide 10: Conclusion
Research Question:
Is a reasonably small increase of the storage space between the yield line and the crosswalk “n_a “ has a significant positive impact on the entry capacity “Cs” ?

## Slide 11: References
Fig. 1: http://ir.nul.nagoya-u.ac.jp/jspui/bitstream/2237/20517/2/10680本文.pdf
Fig. 2: http://ir.nul.nagoya-u.ac.jp/jspui/bitstream/2237/20517/2/10680本文.pdf